Žilina, 29.4.2013
Accelerator physics
4. Proton structure
Ivan Melo

---
Rozptyl elektrónov na protónoch
electron
electron
Elastic scattering
p´
proton
proton
Inelastic scattering
Deep inelastic scattering (DIS)

---
Energy scale of the process
Higher Q2 means the smaller structure seen by photon inside proton
Measure of inelasticity
x = 1 … elastic
x < 1 …. inelastic
x < 0.25 and Q2 > 1 GeV2 …. DIS
fraction of the proton momentum carried by the quark or gluon struck by the photon

---
Odkrývanie štruktúry hmoty
Urýchľovačová fyzika 1
M.Gintner
Ernest Rutherford
1st Baron Rutherford of Nelson
1971 - 1937
α-častice
α-častice
“pudingový” model
“planetárny” model
Hans Geiger, Ernest Marsden
1909

---
Rozptyl elektrónov na protóne (atóme vodíka)
        E << 188 MeV
Rutherford experiment repeated

---
Rozptyl elektrónov na protóne (atóme vodíka)
        E = 188 MeV
R. Hofstadter in 1954 measured the size of the proton - Nobel Prize

---
Rozptyl elektrónov na protóne (atóme vodíka)
        E >> 188 MeV
Deep inelastic scattering

---
Proton as we see it now
Q = + 2/3 + 2/3 -1/3 = +1

---
Summary

---
Parton distribution functions
probability to find a d quark carrying a given
fraction x of the proton momentum
PDF
number of d quarks with x between x1 and x2

---
Parton distribution functions cont'd
one d quark in proton
two u quarks in proton
average momentum fraction
momentum sum rule
36% of p momentum carried by u quarks
18% of p momentum carried by d quarks
46% by gluons and other quarks

---
Proton – proton collisions

---
Proton – proton collisions
Cross sections at LHC (DIS regime) depend on PDFs

---
pT1
pT2
Sum of initial pT = 0
Sum of final pT = 0

---
Chýbajúca priečna hybnosť
If sum of final pT ≠ 0:
1+2+3
1
2
3
Missing pT = Missing ET = ETMiss
ETMiss > 20 GeV (asi neutríno)
ETMiss < 20 GeV (nie neutríno, skôr nedokonalosť detektora)

---
Rapidity and pseudorapidity

---
Invariant mass

---
Discovery of Higgs-like particle
H → γγ
H → ZZ
→ l+l-l+l-

---
Exercises:
1. Show that for LHC protons
2. Show that for partons going into hard interaction
3. Estimate typical CMS collision energy for the two partons from PDFs
4. Show that x = -q2/2q.p can be identified as the fraction of the proton momentum carried by the struck quark (in a frame where the proton has very high energy)

---
5. Do exercise 6.7.1 on p.123 in Bombara, Gintner, Melo Lecture notes
      a) calculate in CompHEP cross section pp → W+d at 2 and 7 TeV
      b) calculate in CompHEP cross section pp → W-u at 2 and 7 TeV
      c) calculate R+- = sigma(W+)/sigma(W-) at 2 and 7 TeV